## Slide 1: DRIVING YOUR CHANGE

## Slide 2: OUR FOCUS
AUTOMOTIVE
CASTING
FRAMING
ASSEMBLY

## Slide 3: What is Gigacasting/ Megacasting/ …
Creation of big structual parts via the extrusion of molten metal under high pressure of 6000 – 9000 tonnes
  Working on presses with over 16.000 tonnes
Main goal:
Reducing the number of parts
Elimination of manufacturing costs due to fewer welding spots and lower amount of parts
Higher rigidity and stiffness

## Slide 4: What is Gigacasting/ Megacasting/ …
Challenges:
  Quality of parts due to the extrusion of molten aluminum
  Faulty casts can cause cracks
Critical voices:
  OEM`s such as BMW are not yet adapting the technice due to quality challenges
  Repair of damage parts is very difficult if not impossible

## Slide 5: Parts for Gigacasting - EV
Car:
Rear & Front structure
Battery pack
Wishbone
Axle carreir
E-Drive:
Stator
Stator housing

## Slide 6: Why Giga casting – car structure
Conventional:
Rear structure is made of 70 pieces of stamped sheet metal
Sealing/ welding/ gluing is necessary to assemble final piece
Stamped parts have a spring back effect which complicates things
Gigacast:
Removing 79 parts per car
Cost reduction of 40% for rear underbody
simplfying mounting operations
Improving build quality

## Slide 7
Conventional Body in White lines have up to 1000 robots for gluing and welding applications
Giga casting:
Number of roboter per line can decrase by 66%
  1000 Robots -> 300 Robots
Reduced floor space due to fewer stations
  Estimation from IDRA -> 20%floor saving
New alloys were necessary to implement the Gigacasting to generate the necessary quality
Why Giga casting – car structure

## Slide 8: OEM investing in / using Gigacasting
EUROPE
ASIA
NORTH AMERICA

## Slide 9: Machine builders Gigacasting
EUROPE
CHINA
JAPAN
Notes: LK-Machinery: https://www.youtube.com/watch?v=qGTBCGeIwVw

## Slide 10: Machine builders for the machining of Mega Casting
Potential suppliers for this process step
 Integrator for unloading for IDRA
 Integrator for unloading for BÜHLER
Integrators for the unloading of Mega Casting machines

## Slide 11: Order books of machine builders Q1 2024
Machine builder | 5.000 T | 6.000 T | 7.000 T | 8.000 T | 9.000 T | 12.000 T | 16.000 T
IDRA |  | Tesla; Linamar; Ford |  |  | Tesla, Hyundai, Volvo |  | 
Bühler |  | Anhui Unique, IKD, Seojin System, Dongguan Econtec; Handtmann |  | Volvo; IKD | Anhui Unique |  | 
LK Machinery | Junling Mould; SPHT | Xpeng; Ruili Group; Tesla; Glovitech; Asiaway; Wencan; SPHT; Yunhai Metals | Xpeng; Wencan; Tuopu; Zeekr | Ruili Group | Ruili Group, Wencan, SPHT | Guangdong Hongtu; SPHT | Guangdong Hongtu
Haitan | Anhui Yongtai |  | Anhui Yongtai | Millison; BAIC Group (Xiaomi) |  |  | 
Yizumi |  |  | Changan, Yunhai Metals |  |  |  | 
Ube & Gauss |  | Ryobi |  |  |  |  | 
ItalPresse-Gauss | Nantong; BMW |  |  |  |  |  | 

## Slide 12: Who supplies whom
OEM & Model | GIGA Press Supplier | Giga Cast Supplier | Integrated Parts | Clamping Force (Ton)
Tesla Model Y | IDRA & LK Machinery | Tesla | Rear | 6.100
Tesla Model Y RWD Berlin | IDRA | Tesla | Front & Rear | 6.100
Tesla Cybertruck | IDRA | Telsa | Front & Rear | 9.200
Xpeng G6 | LK Machinery | Xpeng | Front & Rear | 7.000
Xpeng X9 | LK Machinery | Guangdong HongTu | Front & Rear | 12.000
Zeekr 009 | LK Machinery | Zeekr | Rear | 7.200
Volvo M90 | LK Machinery | Zeekr | Rear | 7.200
Nio ET5 – ES6 | LK Machinery | Wencan | Rear | 6.000
Nio ES8 | Haitian | Millison | Rear | 8.800
Huawei AITO M9 | ? | ? | Front & Rear | 9.000
Xiaomi SU7 | Haitian | Xiaomi (BAIC Group) | Rear | 9.100
Notes: https://haitianinter.com/de/contact/headquarters/

## Slide 13: OEM`s Gigacasting
Volkswagen – Trinity, China
Zeeker – China
Xpeng – China
Xiaomi – China
Volvo – China
Toyota – Japan

## Slide 14: OEM`s Gigacasting
Tesla - Global
NIO – China
Hyundai – Korea
General Motors – USA
Huawei – China
Aisin - Japan
Notes: https://www.autoevolution.com/news/mercedes-benz-vision-eqxx-will-use-body-castings-like-tesla-165817.html

## Slide 15: Volkswagen News – Mega Casting for new car generations

## Slide 16: Application envirounment
Heavy workpieces 100KG or more
Workpiece temperature 250° or more
Unloading with robot
Part has to be pulled out of die casting form
Tesla
XPENG
Xiaomi

## Slide 17: Gripper for Gigacasting
NDA – do not show

## Slide 18: Steps after unloading?
Removing sprue of giga casting
CNC machines or other applications also possible
Laser engraving
Implementing if threads for mounting applications

## Slide 19: CNC machining
Possible clamping solutions for parts
CNC also of battery housings
There are different existing customers from SCHUNK which are building/ integrating such lines