## Slide 2
In modern manufacturing, flexibility and efficiency are key.
SCHUNK's Robot PLUS portfolio is specifically designed to enhance your production processes. It offers a comprehensive range of tool changers, compensation units, and force/torque sensors – developed based on decades of experience.
Partnering with SCHUNK means benefiting from a combination of high-quality products and comprehensive, reliable support that drives and supports your automation projects worldwide

## Slide 3
COMPENSATION UNIT AGM
Modular compensation unit with a compact design and robust guidance
Wide payload range from a few grams to 400 kg
AUTOMATIC TOOL CHANGER CPB
Reliable automatic tool changer with an integrated spring to minimize gaps in the event of air pressure loss
> 200 optional modules for diverse media transmission
AUTOMATIC TOOL CHANGER CPS
Durable tool changer with bolt locking mechanism, equipped with additional pneumatic feed-throughs and mounting surfaces for maximum flexibility
Proven technology with over 20 years of expertise in stationary clamping technology
High-precision 6-axis sensor for detailed force and torque measurements, ideal for demanding process monitoring
<1% measurement accuracy based on the full-scale measurement range
FORCE/TORQUE SENSOR FTS
User-friendly manual change system with extensive complementary portfolio
Up to 478 Nm torque load
MANUAL TOOL CHANGER CMS

## Slide 5: CPS Automatic tool changers

## Slide 6: CPS Made in Germany
Automatic Tool Changer CPS

## Slide 7: CPS Made in Germany
Automatic Tool Changer CPS
  Proven ball-locking mechanism
    Robust technology on the market for more than 30 years
    Locking mechanism made of stainless steel
    Housing made of anodized, high-strength aluminum
    Integrated spring to minimize gap in case of loss of air pressure between master and tool
  Comprehensive accessory portfolio
    Extensive portfolio of optional media modules for all kind of applications
    Wide range of other accessories like storage, sensors etc.
    CTS storage magazine available for each size
  Mix and Match
    With existing SCHUNK SWS tool changers

## Slide 8: CPS Advantages
Automatic Tool Changer CPS
Integrated pneumatic channels
For air and vacuum feed-through
Ball-locking mechanism
No contact necessary before locking the Changer
Self-retaining locking mechanism
Tool remains coupled in case of loss of air
Prepared option for monitoring
Monitoring of locked and unlocked conditions and tool presence
Integrated spring
Gap minimization in case of compressed air drop between master and tool
Housing made of high-strength, hard-anodized aluminum
Long lifetime under high loads
Serialization
Fast and easy tracking
Functional parts made of stainless steel, greased with H1 grease
Prepared for applications also in other environments
Mounting pattern tool side
End effector can be assembled from both sides, maximum flexibility

## Slide 9: CPS Product family with 18 sizes
Automatic Tool Changer CPS
Playload | Size | Preferred product | General data Weight coupled Max. dyn. moment (Mxy/Mz) Amount of screw-on surfaces | Advantages of the preferred product | General data Repeat accuracy Operating pressure Grease
<16kg | CPS 001 CPS 007 CPS 011 | CPS 007 | 0,05 kg … 0,42 kg 2/6 Nm … 35/50 Nm 1x optional modules | Integrated sensors for lock/unlock ISO flange pattern robot side Additional pneumatic ports | 0,015mm 4,5 … 6,9 bar H1 Grease
<35kg | CPS 020 CPS 021 CPS 029 | CPS 021 CPS 029 | 0,86 kg … 1,66 kg 100/80 Nm … 120/150 Nm Up to 3 optional modules | Larger pneumatic ports in the housing G 1/8" instead of M5) Additional flats for modules | 0,015mm 4,5 … 6,9 bar H1 Grease
<50kg | CPS 040 CPS 041 CPS 046 | CPS 040 | 1,87 kg … 2,98 kg 350/350 Nm … 350/400 Nm Up to 5 optional modules | Integrated sensors for lock/unlock | 0,015mm 4,5 … 6,9 bar H1 Grease
<100kg | CPS 060 CPS 071 CPS 076 | CPS 076 | 2,00 kg … 3,68 kg 500/400 Nm … 800/1.800 Nm Up to 2 optional modules | Integrated sensors for lock/unlock Tool presence montoring prepared ISO flange pattern robot side | 0,015mm 4,5 … 6,9 bar H1 Grease
<300 kg | CPS 110 CPS 160 CPS 210 | CPS 110 CPS 160 CPS 210 | 6,60 kg … 9,30 kg 1.000/1.800 Nm … 3.500/1.800 Nm Up to 4 optional modules | Integrated sensors for lock/unlock Tool presence monitoring prepared ISO flange pattern robot side | 0,015mm 4,5 … 6,9 bar H1 Grease
<700 kg | CPS 310 CPS 510 | CPS 310 CPS 510 | 20,00 kg … 28,00 kg 5.000/4.500 Nm … 10.000/4.500 Nm Up to 6 optional modules | Integrated sensors for lock/unlock Tool presence monitoring prepared ISO flange pattern robot side | 0,015mm 4,5 … 6,9 bar H1 Grease

## Slide 10: COS Option modules for all kind of applications
Automatic Tool Changer CPS
SIGNAL | COMMUNICATION | POWER | PNEUMATIC | VACUUM | HYDRAULIC / FLUID
> 200 variants |  |  |  |  | 
Max. 48 VAC / 5 A | EtherNet | Up to 500 VAC / 45 A | NBR form sealings | NBR lip sealings | Up to 150 bar
Digital signals | EtherNet/IP |  | M5, G 1/8“, G 1/4“, G 3/8“, G ½“ | G ¾“, G 1,1/2“, G 2“ | Up to 8 bar
 | ProfiNet |  |  |  | 

## Slide 11: CTS Large portfolio of accessories
CTS C Bolt storage
CTS B passive
(without locking)
CTS P
Pin & Bushing
CTS B aktive
(with locking)
CTS T Storage tray
Automatic Tool Changer CPS
Notes: Focused to the existing Systems
Wording from SWM to CTS
CTS P: 1:1 replacement
CTS C: 1:1 replacement
CTS T: 1:1 replaement

## Slide 12: CPB Automatic tool changers

## Slide 13: CPB Developed and manufactured in Germany
Automatic Tool Changer CPB
Continuous series with 7 sizes (040 to 160), proven SCHUNK bolt-locking mechanism
Payload up to 300 kg, up to 3,000 Nm Mxy moment payload
New developed series of optional modules, can be screwed directly into changer CPB

## Slide 14: CPB From the Machine Table to the Robot
Size | Payload | Weight when coupled | Max. dynamic moment MX / MZ | Sensors inductive for lock/unlock prepared | Sensors inductive for tool presence prepared | Repeat accuracy | Operating pressure | Amount of mounting surfaces for optional modules
 | [kg] | [kg] | [Nm] |  |  | [mm] | [bar] | 
CPB 040 | 20 | 0,41 | 100 / 100 |  |  | 0,015 | 4,5-7 | 2
CPB 050 | 35 | 0,57 | 125 / 125 |  |  |  |  | 2
 |  |  |  |  |  |  |  | 2
CPB 063 | 50 | 1,23 | 350 / 350 |  |  |  |  | 
 |  |  |  |  |  |  |  | 3
CPB 080 | 85 | 1,92 | 500 / 500 |  |  |  |  | 
 |  |  |  |  |  |  |  | 3
CPB 100 | 100 | 3,03 | 800 / 600 |  |  |  |  | 
 |  |  |  |  |  |  |  | 3*
CPB 125 | 200 | 7,22 | 2.000 / 1.000 |  |  |  |  | 
CPB 160 | 300 | 10,56 | 3.000 / 1.500 |  |  |  |  | 3*
*doppeltes Anschraubbild, Anschraubbild J (bsp. für COS R19 Optionsmodul) vorbereitet. |  |  |  |  |  |  |  | 
Automatic Tool Changer CPB

## Slide 15: COB Optional Modules for Media feed-through
Automatic Tool Changer CPB
SIGNAL | COMMUNICATION | POWER | PNEUMATIC | VACUUM
> 50 variants |  |  |  | 
COB S12R/L plus tool coding | COB CB2 | COB CB2 | COB A6M5 | COB V1A
COB P4 | COB CB1 | COB CB3 | COB A618A | COB V2A
COB S8 plus tool coding | COB CIO1 |  | COB A10M5 | 
 | COB CB3 |  |  | 
 | COB CB4 |  |  | 
 | COB CB6 |  |  | 
All optional modules with serialization via DMC code

## Slide 16: CTS B Bolt Storage
Automatic Tool Changer CPB
2 sizes 050 and 085, each available in active (with locking) and passive version (without locking)
Further sizes available from the end of 2025 (up to 250 kg payload)
Screw-on surface “A” prepard on all CPB adapters for mounting the support bolt
CTS B passive
CTS B aktive

## Slide 17: CPB Go beyond
Automatic Tool Changer CPB
Robust, bolt-locking mechanism
  Proven technology in stationary workholding systems for over 20 years
  Internal locking mechanism made of vacuum-hardened stainless steel
  Housing made of anodized, high-strength aluminum
  Integrated spring to minimize gap in case of loss of air between master and tool
More flexibility
  Integrated sensors for monitoring lock/unlock conditions and tool presence
  Newly developed optional modules with universal bolt interface for various media
  Additional integrated pneumatic feed-throughs
  More screw-on surfaces for feed-through modules due the rectangular or hexagonal design
Easy to use
  Integrated ISO flange pattern master and tool side
  Integrated feed-throughs on the adapter can be used radial or axial
  On the adapter side, end effectors can be bolted either onto the quick-change adapter (bolt-up) or through it (bolt-down)

## Slide 18: AGM Modular compensation units

## Slide 19: AGM-Z Mastering tolerances and increasing reliability
Modular Compensation units AGM
AGM-Z 031
AGM-Z 040
AGM-Z 050
AGM-Z 063
AGM-Z 080
AGM-Z 100
AGM-Z 125
AGM-Z 160
AGM-Z 160L
AGM-Z 200
Notes: Folie fertig

## Slide 20: AGM Product family
Broad load capacity range
With the AGM units, loads ranging from a few grams to over 500 kg can be handled
No compromises on the interfering contour
The AGM product family offers the perfect unit for a wide range of applications with 23 sizes
Easy to assemble
The integrated, continuous ISO interface on both the robot and tool sides, from ISO 31,5 to ISO 200, is compatible with most robot types
Always the right compensation behaviour
The wide portfolio enables compensation in XY-, Z-, W-, XYZ-, WZ-direction
Modular Compensation units AGM

## Slide 21: AGM-Z Technical data
Size | Recommended handling weight, vertical | Recommended handling weight, horizontal | Compensation in Z | Net Weight | Monitoring prepared | Standard adapter plates | Modularity: WZ | Modularity: XYZ
 | [kg] | [kg] | [mm] | [kg] |  |  |  | 
AGM-Z 031 | 4 | 4 | 4 | 0,5 | inductive or magnetic |  |  | 
AGM-Z 040 | 8 | 5,7 | 4 | 0,7 |  |  |  | 
AGM-Z 050 | 12 | 12 | 6 | 1,0 |  |  |  | 
AGM-Z 063 | 24 | 18 | 8 | 1,9 |  |  |  | 
AGM-Z 080 | 45 | 32,5 | 10 | 3,6 |  |  |  | 
AGM-Z 100 | 85 | 74 | 15 | 6,0 |  |  |  | 
AGM-Z 125 | 135 | 107 | 15 | 9,7 |  |  |  | 
AGM-Z 160 | 230 | 150 | 15 | 19,3 |  |  |  | 
AGM-Z 160L | 290 | 230 | 20 | 25,2 |  |  |  | 
AGM-Z 200 | 500* | 360* | 20* | 37,8* |  |  |  | 
Modular Compensation units AGM
* Technical Data under reservation

## Slide 22: AGM-XY Mastering tolerances and increasing reliability
Modular Compensation units AGM
AGM-XY 031
AGM-XY 040
AGM-XY 050
AGM-XY 063
AGM-XY 080
AGM-XY 100
AGM-XY 125
AGM-XY 160
AGM-XY 160L
AGM-XY 200
Notes: Ausgleichseinheiten „nur größer“ gezogen, da noch kein BG Rendering verfügbar

## Slide 23: AGM-XY Technical data
Size | Recommended handling weight, vertical | Recommended handling weight, horizontal | Compensation in XY | Net Weight | Monitoring prepared | Adjustable Stroke limitation | Standard adapter plates | Weight compensation | Modularity: XYZ
 | [kg] | [kg] | [mm] | [kg] |  |  |  |  | 
AGM-XY 031 | 4,7 | 2,4 | ± 2 | 0,5 | inductive or magnetic | Abfrage vorbereitet |  | via spring and air cartridge | 
AGM-XY 040 | 9,5 | 5,7 | ± 3 | 0,8 |  |  |  |  | 
AGM-XY 050 | 18 | 9 | ± 4 | 1 |  |  |  |  | 
AGM-XY 063 | 32,5 | 17 | ± 5 | 2 |  |  |  |  | 
AGM-XY 080 | 68 | 25 | ± 7 | 3,6 |  |  |  |  | 
AGM-XY 100 | 130 | 60 | ± 9 | 5,8 |  |  |  |  | 
AGM-XY 125 | 190 | 90 | ± 10 | 10,9 |  |  |  |  | 
AGM-XY 160 | 250 | 130 | ± 12 | 21,8 |  |  |  |  | 
AGM-XY 160L | 350 | 180 | ± 15 | 31,7 |  |  |  |  | 
AGM-XY 200 | 520* | 350* | ± 15* | 41,8* |  |  |  |  | 
Modular Compensation units AGM
* Technical Data under reservation

## Slide 24: AGM-W Mastering tolerances and increasing reliability
AGM-W 050
AGM-W 063
AGM-W 080
Modular Compensation units AGM
Size | Recommended handling weight, vertical | Recommended handling weight, horizontal | Compensation angular | Net Weight | Monitoring prepared | Standard adapter plates | Adjustable weight compensation | Modularity: WZ
 | [kg] | [kg] | [°] | [kg] |  |  |  | 
AGM-W 050 | 8 | 5,5 | ± 5 | 1,2 | inductive or magnetic |  | via control piston | 
AGM-W 063 | 16 | 11 | ± 5 | 1,9 |  |  |  | 
AGM-W 080 | 32 | 22 | ± 5 | 3,2 |  |  |  | 
Notes: Folie fertig

## Slide 25: AGM Combination options thanks to modular series
Advantages:
Lower installation height
Lower weight compared to the combination of single components
AGM-Z
AGM-XY
=
+
AGM-XYZ
AGM-Z
AGM-W
=
+
AGM-WZ
Modular Compensation units AGM

## Slide 26: AGM Offers more…
Most comprehensive range of sensors
Numerous magnetic and inductive monitoring options optionally available for all sizes
Standardized adapter plates In addition to the integrated ISO interface, one adapter plate per size is available for a smaller and one for a larger ISO interface
Effective weight compensation in horizontal applications thanks to patented spring and air cartridges for AGM-XY and AGM-XYZ
Modular Compensation units AGM

## Slide 27: FTS Force torque sensors

## Slide 28: FTS Developed and manufactured in Germany
Force-Torque-Sensors FTS
FTS 047
FTS 056
FTS 070
FTS 085
FTS 105
FTS 125
FTS 160
FTS 200
FTS 250

## Slide 29: Portfolio overview
Sensor
9 Sizes
Interface-Box
1 for all Interfaces
2 Variants (IP)
ISO adapter
3 sizes for each FTS Sensor
Control Center
Robot Control
SPS/PLC
Cable
5 lenghts
2 variants
Force-Torque-Sensors FTS

## Slide 30: Communication Interfaces
EtherCAT
EtherNet & Ethernet/IP
ProfiNET
Force-Torque-Sensors FTS
Ethernet TCP/UDP

## Slide 31: Product Description
FTS | 056 | 600 | 11 | 
Series Force Torque Sensor | Size Outer Diameter Ø56mm | Measurement Range Fz 600 N | Measurement Range Mxyz 11 Nm | 
FTS | IFB | PN |  | 
Series Force Torque Sensor | Interface Face Box | PN ProfiNet EI Ethernet/IP EC EtherCAT EN Ethernet | - IP67 (optional) | 
FTS | C | M8 | M12 | 10
Series Force Torque Sensor | Cable | M8 Size 047 - 085 M12 Size 105 - 250 | M12 Interface Box | 10 m Cable length
Force-Torque-Sensors FTS

## Slide 32: Sizes and Interface plates
Size | Diameter | Measurement Range |  |  | Tool Side | Robot Side Interface Plate Options |  | 
 | Ø | Fx/Fy | Fz | Mx/My/Mz |  | S (small) | M (medium) | L (large)
FTS 047 | 47 mm | 125 N | 300 N | 4,5 Nm | ISO 31,5 | ISO 25 | ISO 31,5 | ISO 40
FTS 056 | 56 mm | 250 N | 600 N | 11 Nm | ISO 40 | ISO 31,5 | ISO 40 | ISO 50
FTS 070 | 70 mm | 500 N | 1200 N | 28 Nm | ISO 50 | ISO 31,5 + ISO 40 | ISO 50 | ISO 63
FTS 085 | 85 mm | 1000 N | 2400 N | 70 Nm | ISO 63 | ISO 50 | ISO 63 | ISO 80
FTS 105 | 105 mm | 2000 N | 4800 N | 175 Nm | ISO 80 | ISO 63 | ISO 80 | ISO 100
FTS 125 | 125 mm | 3200 N | 7800 N | 350 Nm | ISO 100 | ISO 80 | ISO 100 | ISO 125
FTS 160 | 160 mm | 5000 N | 12500 N | 700 Nm | ISO 125 | ISO 100 | ISO 125 | ISO 160
FTS 200 | 200 mm | 10000 N | 20000 N | 1400 Nm | ISO 160 | ISO 125 | ISO 160 | ISO 200
FTS 250 | 250 mm | 16000 N | 32000 N | 2800 Nm | ISO 200 | ISO 160 | ISO 200 | ISO 250
Force-Torque-Sensors FTS

## Slide 33: Advantages and benefits
Standard IP67 for all FTS sizes
LED´s for Power, Communication & Sensor Status integrated in all FTS sizes (with exception size FTS 047)
All FTS sizes with digital signal output, sensor is independent of cable and Interface Box.
The Interface Box has In and Out connections and can therefore be easily integrated into existing network topologies.
Product configuration: SCHUNK Control Center allows easy setup and easy data logging.
Force-Torque-Sensors FTS

## Slide 35: Vorlage SCHUNK Farben
Primärfarben
Akzentfarbe
0–61–106
0–158–224
188–207–0
0–61–106
0–158–224
188–207–0
216–186–34
0–61–106
0–158–224
188–207–0
227–227–227
Fließtext
Highlightfarbe in Tabellen
Darstellung Öl bei Werkzeughaltern
Farbhinterlegungen von leise bis laut (z.B. für Infoboxen)

## Slide 36: Gestaltungselemente
Beispielpluspunkt

## Slide 37: Don’ts
Beschneide oder verdecke bei Anwendungsbilder keine wichtigen Bildinhalte.
Verwende nur Bilder, deren Lizenz du hast.
→ Hinweise auf der nächsten Folie beachten
Das Typenschildlogo muss immer ganz sichtbar sein. Beachte den Schutzraum um das Logo.
Verwende die Akzentfarbe „Lemon“ wirklich nur als Akzent – nicht inflationär.
Überfrachte die Seiten nicht. Achte auf Klarheit und Erfassbarkeit des Inhalts. → Markenwert Klarheit und Qualität
Das „Next-Level-Element“ darf nicht un- proportional skaliert oder verzerrt werden. Der Winkel beträgt immer 27 Grad

## Slide 38: Ressourcen Bildmaterial
Wenn möglich immer SCHUNK-Bildmaterial verwenden, da SCHUNK alle Rechte an den Bildern besitzt. Diese findet ihr im SCHUNK-Media-Pool
Alternativ, wenn SCHUNK-Bildmaterial nicht ausreicht, können Bilder von folgenden Seiten verwendet werden:
pexels.com pixabay.com unsplash.com
Die Inhalte sind kostenlos, lizenzfrei und können ohne Nennung des Urhebers verwendet werden.
Bei der Auswahl ist darauf zu achten, dass die Bilder den SCHUNK-Werten entsprechen.
Keine anstößige, diffamierende, rechtswidrige oder gewaltverherrlichende Inhalte.
Dieses Add-In dient dazu, Medien wie Bilder direkt aus dem Pool in Word oder PowerPoint einzubinden.
Hier geht’s zur Anleitung:
Canto Add-In Anleitung